## Slide 1: Wetland Pollution From Crumb Rubber Athletic Fields
John Sax, 203 Willow Brook Drive

## Slide 2: Background – Loker Field Site and Water Flow
Map shows proposed field, parking lot and approximate location of drainage easements
  Field is in the wetlands buffer zone as shown by red line
  Drainage easement in blue as shown on Town Assessor map
  Carries water through Loker to Willow Brook and on to the Charles River
  2 Conduits carry water under route 30 to Willow Brook Wetlands
  Water flow in Willow Brook from Loker is strong enough to create ripples in the water.

## Slide 3: Where I got my Information and what I found
Reached out to experts
  Professor Gary Mabbott - PHD Analytical Chemistry, St. Thomas University
  Professor Mabbott found and annotated research papers for me and explained the findings to me
  Studies were of chemical leaching from fields with Crumb Rubber material
  Also used EPA guidelines for water pollution levels
  Reference list used for this presentation is at the end of this presentation
  I can forward questions to Professor Mabbott
What we found
  Pending EPA study results, the jury is still out on the hazards of chemicals leached from Crumb Rubber in athletic fields. Some experts believe leached chemical interactions could enhance toxic effects. (reference 1)
  Zinc Leached from Crumb Rubber is toxic to wetlands aquatic life
* Town of Wayland statistics

## Slide 4: The Data
Table below is from Weston and Sampson toxicologist
  Zinc well above background levels because ZnO is used to vulcanize rubber
  Tires typically contain 1-2% Zinc Oxide by weight (Cheng et al. 2014)
4

## Slide 5
Pollutant (P = Priority Pollutant) | CAS Number | Freshwater CMC1 (acute) (µg/L) | Freshwater CCC2 (chronic) (µg/L) | Saltwater CMC1 (acute) (µg/L) | Saltwater CCC2 (chronic) (µg/L) | Publication Year | Notes
Zinc (P) | 7440666 | 120 | 120 | 90 | 81 | 1995 | 
EPA National Recommended Aquatic Life Criteria table
https://www.epa.gov/wqc/national-recommended-water-quality-criteria-aquatic-life-criteria-table
“This table contains the most up to date criteria for aquatic life ambient water quality criteria. Aquatic life criteria for toxic chemicals are the highest concentration of specific pollutants or parameters in water that are not expected to pose a significant risk to the majority of species in a given environment or a narrative description of the desired conditions of a water body being "free from" certain negative conditions. ”
Measured Zinc Levels Leached from Crumb Rubber in Fields
Cheng et al. (2014) (Review Article) (reference 2)
“Overall, the concentrations of heavy metals and organic contaminants in the drainage were low with the exception of Zn, which occurred at concentrations up to near 0.5 mg/L (=500µg/L).”
Moretto (2007) (reference 3)
“A newly installed artificial turf football pitch (with tire rubber crumb infill) located in the Lyon region of France was sampled. Field drainage was collected using a lysimetric system made from a stainless steel sheet buried under the field. The monitoring period was 11 months.” Zn concentration: .074−0.488 mg/L (= 74-488 µg/L)
Cheng and Reinhard (2010) (reference 4)
A one-year old artificial turf field (with tire rubber infill) in northern California of the U.S. was sampled. Drainage was collected using lysimetric systems made from plastic funnels buried under the field. The monitoring period was 1 month. Zn concentration: 0.129−0.473 mg/L (= 129-473 µg/L)

## Slide 6: Loker Field design actually exacerbates Zinc leaching
Weston and Sampson design calls for water storage under field
  Designed to hold water to prevent flooding in major rainstorms
Crumb Rubber layer will marinate in rainwater for extended periods
On warm sunny days Crumb Rubber will reach 140F to 160F
  Like putting water crumb rubber mixture in a crock pot set on medium
Zinc concentration will increase as water evaporates on hot days
  Like boiling tree sap to get Maple syrup
Zinc concentration increases with each rainfall and evaporation cycle
Major rainstorm will flush Zinc laden water into Loker and Willow Brook wetlands
6

## Slide 7: Conclusion
Field design is perfect for maximizing Zinc leaching into wetlands
Zinc levels will exceed EPA standards for aquatic life
Crumb rubber’s only positive feature seems to be that it is cheap
The claim that recently manufactured crumb rubber is better is not based on fact
  Claim has been made is that only US manufactured tires are now used
  Almost all tires are manufactured abroad (6.2% U.S. in 2017)
  There is no data that US made tires are less toxic than foreign made tires
The fixation on Crumb Rubber as the only alternative is irrational
  There are other alternatives
  You can build a really nice field with grass

## Slide 8: References
Environment & Human Health, Inc HTTP://www.ehhi.org/artificial-turf.php
Environmental and Health Impacts of Artificial Turf: A Review Hefa Cheng, Yuanan Hu, and Martin Reinhard, Environ. Sci. Technol., 2014, 48 (4), pp 2114–2129.
Moretto, R. Environmental and Health Assessment of the Use of Elastomer Granulates (Virgin and from Used Tyres) As Filling in Third- Generation Artificial Turf; ADEME/ALIAPUR/Fieldturf Tarkett, 2007.
Cheng, H.; Reinhard, M. Field, Pilot, And Laboratory Studies for the Assessment of Water Quality Impacts of Artificial Turf; Santa Clara Valley Water District: San Jose, CA, 2010.

## Slide 9
Thank You